# INVESTIGATION OF VOC REACTIVITY EFFECTS USING EXISTING REGIONAL AIR QUALITY MODELS

SUMMARY OF PROGRESS

MAY 15-16, 2002

BY

WILLIAM CARTER*

PRINCIPAL INVESTIGATOR

GAIL TONNESEN* AND

GREG YARWOOD**

CONTRIBUTING INVESTIGATORS

*CE-CERT, UNIVERSITY OF CALIFORNIA, RIVERSIDE

** ENVIRON, INTERNATIONAL

# OBJECTIVES

ASSESS VOC REACTIVITY EFFECTS USING AN EXISTING REGIONAL MODELING DATABASE REPRESENTING THE EASTERN U.S.

ASSESS RELATIVE INCREMENTAL OZONE IMPACTS OF VOC MODEL SPECIES WITH RESPECT TO:

VARIATION WITHIN THE MODELING DOMAIN

DERIVATION OF VARIOUS REACTIVITY METRICS

COMPARISON WITH REACTIVITIES CALCULATED USING EKMA MODELS

PREDICTIONS OF EFFECTS OF SELECTED LARGE SCALE SUBSTITUTIONS

ASSESS APPROACHES FOR DERIVING A GENERAL REACTIVITY SCALE REPRESENTING REGIONAL O3 IMPACTS

# CRC-NARSTO MODELING DATABASE

| MODEL: | CAMx VERSION 3.01 WITH DDM |
| --- | --- |
| EPISODE DATES: | JULY 7-15, 1995 (DATA FOR 11th-14th USED IN ASSESSMENT) |
| EMISSIONS: | EPA NET96 |
| MET DATA: | MM5 |
| MECHANISM: | UPDATED CB4 (ETHANE ADDED) |

(Analysis of fine grid data still underway. Current analysis uses 4 and 12 km data averaged into the 36 KM grids.)

# CARBON BOND 4 MECHANISM

## ADVANTAGES

LEAST EXPENSIVE TO USE FOR INITIAL STUDY

WIDELY USED

REPRESENTS MOST OF THE IMPORTANT CLASSES OF REACTIVE VOCs

## DISADVANTAGES

OUT-OF-DATE (DEVELOPED IN1989)

HIGHLY CONDENSED. CANNOT BE USED TO ASSESS MOST INDIVIDUAL VOCs

INAPPROPRIATE OR NO REPRESENTATION OF SOME IMPORTANT TYPES OF VOCs:

INTERNAL ALKENES (only products represented; effects of initial OH and O3 reaction ignored)

TOLUENE (reactivity characteristics significantly different than predicted using current mechanisms)

RADICAL INHIBITING VOCs (not represented)

MAY BE MORE SENSITIVE TO RADICAL EFFECTS THAN CURRENT MECHANISM

## NEVERTHELESS, CB4 PROBABLY SUITABLE FOR INITIAL QUALITATIVE ASSESSMENT OF VARIABILITY OF REACTIVITY WITH MODELING DOMAIN

# PHASE1: DDM CALCULATIONS

DECOUPLED DIRECT METHOD (DDM) USED TO CALCULATE SENSITIVITIES OF SURFACE O3 CONCENTRATIONS TO CHANGES IN EMISSIONS

SENSITIVITIES CALCULATED AS FUNCTION OF TIME AND SPACE AND OUTPUT AS HOURLY AVERAGES FOR ALL GROUND LEVEL CELLS.

FIRST DDM CALCULATION:

SENSITIVITY TO TOTAL VOC AND NOx EMISSIONS

RESULTS GIVE PPM O3 CHANGE RESULTING FROM 100% CHANGE IN EMISSIONS (IF LINEAR)

SECOND DDM CALCULATION:

SENSITIVITY TO SURFACE EMISSIONS OF CO AND 9 VOC MODEL SPECIES VARIED.

SAME TIME AND SPACE DISTRIBUTION AS TOTAL ANTHROPOGENIC VOC

RESULTS GIVE PPM O3 CHANGE FROM 100% CHANGE IN ANTHROPOGENIC VOC CARBON EMISSIONS AS THE SPECIES (IF LINEAR)

THE SENSITIVITIES OF O3 TO MODEL SPECIES EMISSIONS ARE THE SAME AS THE INCREMENTAL REACTIVITIES OF THESE MODEL SPECIES

CARBON BOND 4 MODEL SPECIES

# WHOSE OZONE SENSITIVITIES WERE DETERMINED

| SPECIES | APPROXIMATELY REPRESENTATIVE OF |
| --- | --- |
| PAR | C4 - C6 ALKANES |
| ETH | ETHENE (EXPLICIT) |
| OLE | PROPENE (PRIMARILY) |
| TOL | NO SPECIFIC COMPOUND. MAY BE INDICATIVE OF COMPOUNDS WITH VERY NOx SENSITIVE REACTIVITIES (E.G., PHENOLS, STYRENES) |
| XYL | XYLENES |
| FORM | FORMALDEHYDE (EXPLICIT) |
| ALD2 | ACETALDEHYDE (EXPLICIT) |
| ETOH | ETHANOL (EXPLICIT) |
| ETHA | ETHANE (ADDED FOR THIS STUDY) |
| CO | CARBON MONOXIDE (EXPLICIT) |

OZONE IMPACT METRICS USED

# IN INITIAL ANALYSIS

IMPACTS BASED ON EFFECTS OF SPECIES ON DAILY MAXIMUM 1-HOUR AND 8-HOUR AVERAGE O3

FOLLOWING CELLS NOT INCLUDED IN ANALYSIS:

CELLS WHERE MAXIMUM O3 LESS THAN CUTOFF

80 PPB CUTOFF FOR 1-HOUR AVERAGE

60 PPB CUTOFF FOR 8-HOUR AVERAGE

CELLS WITH ZERO ANTHROPOGENIC EMISSIONS (I.E., CELLS OVER WATER)

REACTIVITIES DERIVED RELATIVE TO REACTIVITIES OF TOTAL ANTHROPOGENIC VOC EMISSIONS MIXTURE (BASE ROG)

GIVES BENEFITS OF REDUCING A SINGLE VOC COMPARED TO REDUCING ALL VOCs EQUALLY

BASE ROG SENSITIVITIES DERIVED FROM SENSITIVITIES OF COMPONENT SPECIES

BASE ROG COMPOSITION DERIVED FROM EPA REGIONAL EMISSIONS DATABASE

TOTAL VOC SENSITIVITIES COULD NOT BE USED BECAUSE THEY INCLUDED BIOGENIC VOCs

4 GLOBAL RELATIVE REACTIVITY METRICS DERIVED

MINIMUM SUBSTITUTION ERROR (2 METHODS)

REGIONAL MIR

REGIONAL MAXIMUM O3

# COMPOSITION OF BASE ROG MIXTURE USED TO DERIVE RELATIVE REACTIVITIES

| CB4 MODEL SPECIES: CARBON BASIS |  |
| --- | --- |
| CB4 MODEL SPECIES: REACTIVITY BASIS (EKMA MIR SCALE) |  |

(BASED ON NEW EMISSIONS ASSIGNMENTS 5/02)

# GLOBAL RELATIVE REACTIVITY METRIC #1

# MINIMUM SUBSTITUTION ERROR: BASE ROG FOR SPECIES

## DEFINITION

RELATIVE REACTIVITY TO MINIMIZE SUBSTITUTION ERROR FROM REACTIVITY-BASED SUBSTITUTION OF THE BASE ROG FOR THE MODEL SPECIES

SUBSTITUTION ERROR =

Σcells [RR(Species)·IRcell(Base ROG) - IRcell(Species)]2

## ADVANTAGES

WEIGHS CELLS THAT ARE SENSITIVE TO VOCs MORE HIGHLY WHILE TAKING THE MANY CELLS WITH LOWER SENSITIVITIES INTO ACCOUNT

REPRESENTATIVE OF STRATEGIES INVOLVING REPLACING HIGHLY REACTIVE VOCs WITH VOCs OF AVERAGE REACTIVITY

REACTIVITIES OF MIXTURES ARE LINEAR SUMS OF REACTIVITIES OF COMPONENTS

## DISADVANTAGES

MAY NOT OPTIMALLY WEIGH CONTRIBUTIONS OF DIFFERENT TYPES OF REGIONS

NOT A PARTICULARLY REALISTIC SUBSTITUTION FOR EXEMPTION ISSUES

# GLOBAL RELATIVE REACTIVITY METRIC #2

# MINIMUM SUBSTITUTION ERROR: SPECIES FOR BASE ROG

## DEFINITION

RELATIVE REACTIVITY TO MINIMIZE SUBSTITUTION ERROR FROM REACTIVITY-BASED SUBSTITUTION OF THE MODEL SPECIES FOR THE BASE ROG

SUBSTITUTION ERROR =

Σcells [IRcell(Base ROG) - IRcell(Species)/RR(Species)]2

## ADVANTAGES

WEIGHS CELLS THAT ARE SENSITIVE TO VOCs MORE HIGHLY WHILE TAKING THE MANY CELLS WITH LOWER SENSITIVITIES INTO ACCOUNT

REPRESENTATIVE OF STRATEGIES INVOLVING SUBSTITUTIONS OF CURRENT EMISSIONS WITH LOW REACTIVITY VOCs

## DISADVANTAGES

MAY NOT OPTIMALLY WEIGH CONTRIBUTIONS OF DIFFERENT TYPES OF REGIONS

REACTIVITIES OF MIXTURES ARE NOT LINEAR SUMS OF THOSE OF COMPONENTS

DIVERGENT RESULTS OBTAINED FOR VOCs WHOSE REACTIVITIES ARE SCATTERED AROUND ZERO

# GLOBAL RELATIVE REACTIVITY METRIC #3

# REGIONAL MAXIMUM INCREMENTAL REACTIVITY

## DEFINITION

USE REACTIVITIES AT THE LOCATION WHERE THE INCREMENTAL REACTIVITY OF THE BASE ROG AT THE TIME OF THE O3 MAXIMUM IS THE HIGHEST

## ADVANTAGES

COMPARABLE TO THE WIDELY-USED CARTER (1994) MIR SCALE

REPRESENTATIVE OF IMPACTS IN REGIONS MOST SENSITIVE TO ANTHROPOGENIC VOC CONTROLS

## DISADVANTAGES

NOT A TRUE GLOBAL METRIC. DERIVED FROM IMPACTS IN ONLY ONE TYPE OF REGION

REPRESENTS ONLY A SMALL FRACTION CELLS IN MODELING DOMAIN

DOES NOT REPRESENT IMPACTS IN CELLS WITH THE HIGHEST O3

DOES NOT REPRESENT IMPACTS IN THE MANY NOx-LIMITED CELLS

# GLOBAL RELATIVE REACTIVITY METRIC #4

# REGIONAL MAXIMUM OZONE REACTIVITY

## DEFINITION

USE REACTIVITIES AT THE TIME AND LOCATION OF THE DOMAIN-WIDE O3 MAXIMUM

## ADVANTAGES

ADDRESSES NEEDS TO REDUCE PEAK O3, WHICH IS OF REGULATORY INTEREST

SIMPLEST METRIC TO IMPLEMENT

## PROBLEMS

NOT A TRUE GLOBAL METRIC. DERIVED FROM IMPACTS IN ONLY ONE LOCATION

NOT NECESSARILY REPRESENTATIVE OF “MOIR” CONDITIONS AS DEFINED BY CARTER (1994)

REACTIVITY CHARACTERISTICS OF THE HIGHEST O3 CELL CAN VARY SIGNIFICANTLY DEPENDING ON THE EPISODE

THE DOMAIN-WIDE MAXIMUM O3 MAY BE INSENSITIVE TO ANTHROPOGENIC VOCs

# EKMA REACTIVITY SCALES FOR COMPARISON WITH REGIONAL MODEL REACTIVITIES

SAME EKMA SCENARIOS AND CALCULATION METHODS AS USED TO DERIVE “CARTER” REACTIVITY SCALES (CARTER, 1994; CARTER, 2000)

SAME VERSION OF CB4 AS USED IN THE CAMx REGIONAL MODEL CALCULATIONS

RELATIVE REACTIVITIES USE SAME BASE ROG MIXTURE AS USED FOR REGIONAL METRICS

MIR SCALE

AVERAGES OF INCREMENTAL REACTIVITIES IN THE SCENARIOS WITH NOx ADJUSTED TO YIELD MAXIMUM BASE ROG REACTIVITY

ANALOGOUS TO REGIONAL MIR METRIC

MOIR SCALE

AVERAGES OF INCREMENTAL REACTIVITIES IN THE SCENARIOS WITH NOx ADJUSTED TO YIELD MAXIMUM PEAK O3 CONCENTRATIONS

NOT NECESSARILY ANALOGOUS TO REGIONAL MAXIMUM O3 METRIC

BASE CASE SCALES

RELATIVE REACTIVITIES DERIVED TO MINIMIZE SUBSTITUTION ERRORS IN THE BASE CASE (UNADJUSTED NOx) SCENARIOS

ANALOGOUS TO MINIMUM SUBSTITUTION ERROR METRICS #1 AND #2 FOR 1-HOUR AVG.

GEOGRAPHICAL DOMAIN FOR

# MAXIMUM 1-HOUR AVERAGE O3 AND ANTHROPOGENIC VOC SENSITIVE REGIONS

JULY 11

GEOGRAPHICAL DOMAIN FOR

# MAXIMUM 1-HOUR AVERAGE O3 AND ANTHROPOGENIC VOC SENSITIVE REGIONS

JULY 14

GEOGRAPHICAL DOMAIN FOR

# MAXIMUM 8-HOUR AVERAGE O3 AND ANTHROPOGENIC VOC SENSITIVE REGIONS

JULY 14

# MAXIMUM 1-HOUR AVERAGE OZONE SENSITIVITIES TO VOC AND NOx

Maximum 1-HOUR AVERAGE QUANTIFICATION

(Cells with Maximum 1-Hour Average O3 < 80 ppb

and with Zero Emissions are Excluded)

SENSITIVITIES TO BASE ROG (REPRESENTING ANTHROPOGENIC VOCs)

# VS. SENSITIVITIES TO TOTAL VOCs

1-HOUR AVERAGE QUANTIFICATION

ALL CELLS WHERE MAXIMUM 1-HOUR O3 > 80 PPB

DISTRIBUTION OF BASE ROG (ANTHROPOGENIC)

/ TOTAL VOC SENSITIVITY RATIO

[O3 SENSITIVITY TO BASE ROG]

[O3 SENSITIVITY TO ALL VOCs]

(MAXIMUM 1-HOUR AVERAGE QUANTIFICATION)

Cells with total VOC sensitivity < 0.001 excluded

# REACTIVITY CHARACTERISTICS OF EPISODE DAYS

| EPISODE DAY | 7/11 | 7/12 | 7/13 | 7/14 |
| --- | --- | --- | --- | --- |
| DOMAIN-WIDE OZONE MAXIMUM (ppb) |
| Peak 1-Hr Avg. O3 | 165 | 162 | 187 | 175 |
| Peak 8-Hr Avg. O3 | 127 | 126 | 139 | 139 |
| HIGH OZONE CELLS |
| 1-Hr Avg. > 80 ppb | 18% | 22% | 25% | 25% |
| 1-Hr Avg. > 120 ppb | 1% | 1% | 2% | 4% |
| 8-Hr Avg. > 60 ppb | 32% | 37% | 38% | 36% |
| 8-Hr Avg. > 80 ppb | 7% | 7% | 10% | 12% |
| CELLS MORE SENSITIVE TO VOCs THAN NOx |
| 1-Hour Avg. Quant. | 32% | 23% | 27% | 25% |
| 8-Hour Avg. Quant. | 25% | 29% | 33% | 24% |

# ETHANE VS. BASE ROG SENSITIVITIES

1-HOUR DAILY MAXIMUM O3

8-HOUR DAILY MAXIMUM O3

# 1-HOUR MAXIMUM O3 SENSITIVITY EXAMPLES

XYLENE VS BASE ROG

FORMALDEHYDE VS BASE ROG

# CB4 “TOL” SPECIES VS. BASE ROG SENSITIVITIES

1-HOUR DAILY MAXIMUM O3

8-HOUR DAILY MAXIMUM O3

# SUMMARY OF EKMA AND SELECTED REGIONAL RELATIVE REACTIVITIES FOR CB4 SPECIES

| Model Species | Relative Reactivities (Carbon Basis) Effect on Maximum 1-Hour O3 |
| --- | --- |
|  | MIR Scales |  | Minimum Subst. Error: ROG for VOC |
|  | EKMA | Regional | EKMA | Regional |
| PAR | 0.40 | 0.65 ± 0.08 | 0.59 | 0.76 ± 0.07 |
| ETH | 2.7 | 2.8 ± 0.2 | 3.0 | 2.9 ± 0.1 |
| OLE | 5.6 | 5.1 ± 0.4 | 5.8 | 5.0 ± 0.3 |
| TOL | 0.6 | 0.33 ± 0.07 | -3.0 | -0.12 ± 0.12 |
| XYL | 2.7 | 2.0 ± 0.2 | 2.2 | 1.6 ± 0.2 |
| HCHO | 6.6 | 4.1 ± 0.6 | 5.9 | 3.5 ± 0.5 |
| ALD2 | 3.5 | 2.6 ± 0.3 | 3.7 | 2.6 ± 0.2 |
| Ethane | 0.09 | 0.17 ± 0.03 | 0.16 | 0.23 ± 0.03 |
| Ethanol | 0.76 | 0.7 ± 0.2 | 1.10 | 0.89 ± 0.08 |
| CO | 0.03 | 0.06 ± 0.01 | 0.06 | 0.09 ± 0.01 |

Regional data are averages of the results for the four episode-days

# SUMMARY OF EKMA AND SELECTED REGIONAL RELATIVE REACTIVITIES SELECTED COMPOUNDS

| Compound | Relative Reactivities - Mass Basis |
| --- | --- |
|  | MIR |  | Min Subst. Err. #1 |
|  | SAPRC | CB4 |  | CB4 |
|  | EKMA | EKMA | Regional Average |  | EKMA | Regional Average |
| Ethane | 0.11 | 0.10 | 0.19 |  | 0.16 | 0.26 |
| n-Butane | 0.46 | 0.47 | 0.76 |  | 0.65 | 0.89 |
| Ethylene | 3.2 | 3.2 | 3.5 |  | 3.6 | 3.6 |
| Propene | 4.0 | 4.6 | 4.3 |  | 4.9 | 4.4 |
| m-Xylene | 3.7 | 3.5 | 2.7 |  | 2.6 | 2.1 |
| Formaldehyde | 3.1 | 3.7 | 2.4 |  | 3.1 | 2.0 |
| Acetaldehyde | 2.4 | 2.7 | 2.1 |  | 2.8 | 2.0 |
| Ethanol | 0.59 | 0.56 | 0.58 |  | 0.76 | 0.66 |
| CO | 0.020 | 0.020 | 0.039 |  | 0.034 | 0.055 |

Note:

Only compounds that are reasonably well represented in the CB4 calculations are listed.

“SAPRC” is SAPRC-99

CB4 n-butane is 4 PAR, propene is OLE + PAR

“Min. Subst. Error #1” is ROG for VOC substitution

# EFFECT OF KINETIC REACTIVITY ON DIFFERENCES BETWEEN REGIONAL AND EKMA RELATIVE REACTIVITIES

# PRELIMINARY LARGE SCALE SUBSTITUTION CALCULATIONS

## CALCULATION 1

ALL ANTHROPOGENIC VOCS REMOVED

RESULTS ARE COMPARED WITH PREDICTIONS USING LINEAR APPROXIMATION AND BASE ROG REACTIVITIES FROM DDM CALCULATION

## CALCULATION 2

ALL ANTHROPOGENIC VOCs REPLACED BY ETHANE ON A CARBON FOR CARBON BASIS

RESULTS ARE COMPARED WITH CALCULATION WITH ALL ANTHROPOGENIC VOCs REMOVED TO DETERMINE EFFECT OF ETHANE ADDITION

RESULTS ARE COMPARED WITH EFFECTS OF ETHANE ADDITION PREDICTED BY DDM CALCULATION OF ETHANE REACTIVITY

ONLY DATA FOR JULY 13 AND 14 ARE CURRENTLY ANALYZED

# MAXIMUM 1-HOUR AVERAGE O3 REDUCTION FROM REMOVING ALL ANTHROPOGENIC VOCs

JULY 14

# PLOT OF CHANGE IN MAXIMUM 1-HOUR O3 FROM REMOVING ANTHROPOGENIC VOCs VS. (O3 PREDICTED BY BASE ROG REACTIVITY

DEPENDENCE OF RATIO ON BASE ROG REACTIVITY

# ERROR IN LINEAR APPROXIMATION PREDICTION OF (O3 FOR ANTHROPOGENIC VOC REMOVAL

[DIRECT CALC] – [DDM ESTIMATE (BASE ROG)]

[DIRECT CALC]

(FOR CELLS WHERE (O3 > 1 PPB ONLY)

# MAXIMUM 1-HOUR AVERAGE O3 INCREASE FROM ADDING BACK ETHANE TO REPLACE THE ANTHROPOGENIC VOCs THAT WERE REMOVED

JULY 14

# ERROR IN LINEAR APPROXIMATION PREDICTION OF (O3 FOR ADDING BACK ETHANE AFTER ANTHROPOGENIC VOCs REMOVED

[DIRECT CALC] – [ETHANE I.R. ESTIMATE]

[DIRECT CALC]

(FOR CELLS WHERE (O3 > 0.5 PPB ONLY)

# SPATIAL DISTRIBUTION OF O3 CHANGES CAUSED BY REPLACING EACH CARBON IN THE BASE ROG WITH 3.9 CARBONS OF ETHANE

THE OPTIMUM FACTOR WAS DERIVED FROM THE MINIMUM ETHANE-FOR-VOC SUBSTITUTION ERROR FOR ALL CELLS (INCLUDING OVER H2O AND LOW O3)

O3 CHANGE IN PPB IF 100% SUBSTITUTED (IF LINEAR)

# PRELIMINARY CONCLUSIONS

NOx CONTROL IS MORE EFFECTIVE THAN VOC CONTROL IN MOST OF THIS MODELING DOMAIN

BIOGENIC VOCs DOMINATE OVER ANTHROPOGENICS IN MOST IN MOST OF THIS MODELING DOMAIN

RELATIVE REACTIVITIES ARE HIGHLY VARIABLE, BUT VARIABILITY IS LESS IN MORE VOC-SENSITIVE CELLS

RELATIVE REACTIVITIES VARY FROM DAY TO DAY IN ANY GIVEN REGION

THE MINIMUM SUBSTITUTION ERROR (MSE) METHOD PROVIDES A MEANS TO DERIVE REACTIVITY METRICS BASED ON VARYING REGIONAL IMPACTS

THE MINIMUM SUBSTITUTION ERROR AND REGIONAL MIR METRICS GIVE CONSISTENT RESULTS FOR MOST CB4 SPECIES EXCEPT TOL

THE REGIONAL MAXIMUM O3 METRIC DOES NOT GIVE CONSISTENT REACTIVITY RESULTS

EKMA-BASED REACTIVITY SCALES ARE REASONABLY CONSISTENT WITH REGIONAL MSE AND MIR METRICS, BUT SOME BIASES EXIST

EKMA SCALES OVERESTIMATE AROMATIC AND FORMALDEHYDE REACTIVITIES (but this needs to be verified using current mechanisms)

EKMA SCALES UNDERESTIMATES REACTIVITIES OF SLOWLY REACTING SPECIES (E.G., ETHANE)

# PRELIMINARY CONCLUSIONS (CONTINUED)

NEED TO VERIFY THESE CONCLUSIONS WITH ANALYSIS OF FINE GRID DATA

NEED TO TEST THE ASSUMPTION THAT THE BASE ROG SENSITIVITIES CAN BE USED TO ESTIMATE SENSITIVITIES TO TOTAL ANTHROPOGENIC VOCs

PRELIMINARY CONCLUSIONS FROM 100% ANTHROPOGENIC VOC REMOVAL CALCULATION

MAXIMUM (O3 IS ~70 PPB, BUT ONLY ~10% OF THE CELLS HAVE (O3 > ~5 PPB, 2%>15 PPB.

EFFECT PREDICTED REASONABLY WELL BY DDM EXCEPT SOME CELLS LOW BASE ROG SENSITIVITY PREDICTED TO HAVE LARGE (O3.

PRELIMINARY CONCLUSIONS FROM 100% ETHANE SUBSTITUTION CALCULATION ON EFFECT OF ADDING BACK ETHANE AFTER ANTHRO. VOCs REMOVED

MAXIMUM (O3 IS ~8 PPB, BUT ONLY ~10% OF THE CELLS HAVE (O3 > 2 PPB

INCREMENTAL REACTIVITY ANALYSIS PREDICTS (O3 REASONABLY WELL IN ~95% OF THE CELLS

PREDICTIONS OF EFFECTS OF “OPTIMUM” SUBSTITUTIONS BASED ON INCREMENTAL REACTIVITY ANALYSIS STILL NEED TO BE TESTED WITH LARGE SCALE SUBSTITUTION CALCULATIONS

NEED TO FINALIZE WHICH OF THE LARGE SCALE SUBSTITUTION CALCULATIONS WILL BE CONDUCTED

# Text boxes

36 KM

GRIDS

12 KM

4 KM